## Slide 1
Reconstruction with DREAM.3D
Read in EBSD map slices
    align slices, cleanup
Segment Grains, group together pixels of consistent orientation
    grain Id
Mesh & Smoothing, label grain interfaces to form interface network
    triangle label
Statistics
Read in EBSD map slices
  align slices, clean up
Segment grains
  group pixels of constant orientation and assign grain ID
Mesh & Smoothing
  represent grain boundaries with smoothed triangles
Statistics
Volumetric
Phases
Grains
Interfacial
Grain boundaries
Figure 1. Flow chart of DREAM.3D data processing

## Slide 2
Read in EBSD map slices
  align slices, clean up
Segment grains
  group pixels of constant orientation and assign grain ID
Mesh & Smoothing
  represent grain boundaries with smoothed triangles
Statistics
Volumetric
  Phases
  Grains
    grain sizes, grain orientation …
Interfacial
  Grain boundaries
    triangle label, triangle normal, triangle area …
Figure 1. Flow chart of DREAM.3D data processing

## Slide 3
Find the triangles on triple line.
Check its node type, it 2 of the 3 nodes have type 3, keep it.
Sort the triangles into groups of 3.
Find the triangles groups that share 2 common vertex.
first sort vertex of every triangle to increase order, then check if (1,2), (1,3), (2,3) is the same
If the group contain more than 3 triangles, ignore this group.
for j = 1:#groups
for i = 1:3
Get TriNormal of the other two triangles in the group as N1 and N2
DihedralAngle_Ttr((j-1)+i) = (angle between N1 and N2, adjusted to 0-180°)
end
end
Read input data
  triangle normal
  triangle file
  triangle node type file
Find all the triangles sitting on a triple line
Sort the triple line triangles into groups of three
Find dihedral angles within each group